## Slide 1
LoRa

## Slide 2
01
02
03
LoRa Technology
LoRa Applications
LoRa Module Hands-on
LoRa Feature
LoRa Radio Freq
LoRaWan
04
LoRa Application Hands-on
Setup Development environment
Libraries
UnConfirmed Up Demo
Confirmed Up Hand-on
Downlink Demo
H/W Introduce
AT Commands
Hands-on
Appendix
LoRa Gateway

## Slide 3: LoRa Technology
LoRa Feature
LoRa Radio Freq
LoRaWan

## Slide 4
LoRa Feature

## Slide 5
LoRa is a Low-Power Wireless Wide Area Network (LPWAN) that provides very wide coverage with coverage over 10 km and a communication speed of up to several kilobits per second (kbps).
LPWAN can have up to many years of battery life.
LPWAN technology, is mainly used as a dedicated network technology for low power internet of things (IoT). (For example, water, gas, electric meter monitoring)
Types of LPWAN include LoRa, Sigfox, LTE-MTC, and NB-IoT.
LoRa and Sigfox are ISM license-free band. And LTE Machine-Type communications (LTE-MTC) and Narrowband Internet of Things(NB-IoT) technologies that use mobile licensed bands.
What is LoRa?

## Slide 6
Why LoRa?
Wide Coverage
Low chip price
Low power

## Slide 7
LoRa technology
LoRa is based on Chirp Spread Spectrum. Chirp signal is the technology used for existing radar and distance / position positioning, and is the core of LoRa technology that ables long range and low power.
It is an advantage that frequency / time error and synchronization can be adjusted quickly.
High reliability
Multipath resistant
Low power consumption
Low latency

## Slide 8
LoRa network structure
The LoRa network structure consists of LoRa device, LoRa gateway, a network server, and an App Server.

## Slide 9
LoRa network structure (Korea SK Telecom)

## Slide 10
LoRa Radio Freq

## Slide 11
LoRa Data Rate
There are 6 data rates from DR0 to DR5, and LoRa device operates with one of 6 DRs.
Spreading Factor, Maximum Data Rate, and Maximum Application Payload Size for each DR are as follows.

## Slide 12
LoRa ADR (Adaptive data rate scheme)
The lower DataRate, the longer distance communication is possible, but the longer the channel occupation time is.
Therefore, the LoRa Network Server reduces the speed of the devices that are far away by the receiving sensitivity, and increases the devices that are near the distance.

## Slide 13
LoRa ISM Band
The LoRa ISM Band differs from country to country and must comply with the country's frequency law.

## Slide 14
LoRa ISM Band - India
Channel | Frequency | Modulration /BW
0 | 865.400 Mhz | MultiSF / 125 Khz
1 | 865.600 Mhz | MultiSF / 125 Khz
2 | 865.800 Mhz | MultiSF / 125 Khz
3 | 866.000 Mhz | MultiSF / 125 Khz
4 | 866.200 Mhz | MultiSF / 125 Khz
5 | 866.400 Mhz | MultiSF / 125 Khz
6 | 866.600 Mhz | MultiSF / 125 Khz
7 | 866.800 Mhz | MultiSF / 125 Khz
Rx2 | 865.200 Mhz | SF12 / 125Khz

## Slide 15
LoRa ISM Band – EU868
Channel | Frequency | Modulration /BW
0 | 868.100 Mhz | MultiSF / 125 Khz
1 | 868.300 Mhz | MultiSF / 125 Khz
2 | 868.500 Mhz | MultiSF / 125 Khz
3 | 868.700 Mhz | MultiSF / 125 Khz
4 | 868.900 Mhz | MultiSF / 125 Khz
5 | 869.100 Mhz | MultiSF / 125 Khz
… | … | …
15 | 871.100 Mhz | MultiSF / 125 Khz
Rx2 | 869.525 Mhz | SF9 / 125Khz

## Slide 16
LoRa ISM Band – KR920
Channel | Frequency | Modulration /BW
0 | 920.900Mhz | MultiSF / 125 Khz
1 | 921.100Mhz | MultiSF / 125 Khz
2 | 921.300 Mhz | MultiSF / 125 Khz
3 | 921.500 Mhz | MultiSF / 125 Khz
4 | 921.700 Mhz | MultiSF / 125 Khz
5 | 921.900 Mhz | MultiSF / 125 Khz
… | … | …
12 | 923.300 Mhz | MultiSF / 125 Khz
Rx2 | 921.900 Mhz | SF12 / 125Khz

## Slide 17
LoRaWan

## Slide 18
LoRaWan Structure

## Slide 19
LoRa Device Classes

## Slide 20
LoRa Device Class A

## Slide 21
LoRa Device Class B

## Slide 22
LoRa Device Class C
Rx2
Rx2
Rx1

## Slide 23
LoRa MAC Layer
MAC Payload : The length is variable and consists of FHDR, Fport, and FRMPayload.
MIC : Message Integrity Check(4bytes), Used to check the integrity of MAC messages
FHDR : Frame Header(7~22bytes), Variable length includes DevAddr, FCtrl, FCnt, Fopts
DevAddr : Device Address(4bytes), When the device joins the system, to be allocated.
FCtrl : Frame Control(1bytes), Field that defines the characteristics of the frame.

## Slide 24
LoRa service utilizes DevEUI and AppEUI to distinguish between devices and services. DevEUI is a standard established by the IEEE, Global Unique.
LoRa Service ID System
ID | Length | Form | Release by | Comment
DevEUI | 64bit | 16bytes hex string | IEEE | IEEE MAC Address
AppEUI | 64bit | 16bytes hex string | LoRa network licensee | Service separator
AppKEY | 128bit | 32bytes hex string | LoRa network licensee | Security Key

## Slide 25
LoRa Security Over-The-Air-Activation (OTAA)
AppEUI(8) |
DevEUI(8) |
DevNonce(2)
AppNonce(3) |
NetID(3) |
DevAddr(4) |
DLSetting(1) |
RXDelay(1) |
CFList(16, op)

## Slide 26
LoRa Security Over-The-Air-Activation (OTAA)
LoRa Device
DevEUI AppEUI AppKey
LoRa Server
Join Request
Join Accept
DevEUI AppEUI AppKey

## Slide 27
LoRa Security Activation by Personalization (ABP)
Using ABP join mode requires the user to define the following values and input them into the device
DevADDR, APPSKEY, NWSKEY

## Slide 28
LoRa Security

## Slide 29
LoRa Data Uplink - Confirmed
Confirmed Uplink replies ACK from LoRa server in Rx slot after Uplink.
If ACK is not received, it retransmits the number of times set up (up to 8 times).

## Slide 30
LoRa Data Uplink - Confirmed
1st Confirmed Up
Ack Rx
2nd Confirmed Up
Ack Rx
The device transmits the number of retrans times until it receives an Ack.
.
.
.

## Slide 31
LoRa Data Uplink - Unconfirmed
Unconfirmed Uplink does not receive ACK.
The figure above shows the Unconfirmed Uplink, receiving the Confirmed Downlink from the server, and sending the ACK again.

## Slide 32
LoRa Data Uplink - Unconfirmed
1st UnConfirmed Up
Transmission until the number of Retrans
or Downlink Data
.
.
.
2nd UnConfirmed Up
3rd UnConfirmed Up
4th UnConfirmed Up

## Slide 33: LoRa ApPLICATIONS

## Slide 34
LoRa Application
Gas AMI
Tracker
Monitoring
Shock detector

## Slide 35
LoRa Application
Smart Farm

## Slide 36
LoRa Application

## Slide 37: LoRa Module hand-on
H/W Introduce
AT Commands
Hands-on

## Slide 38
H/W Introduce

## Slide 39
WIZLoRa100
Module integrates Semtech SX1276 and stm32L.
Offer user an serials At commands with UART Interface
Long Range LoraWAN operating in the 868 MHz or 915 MHz frequency bands
Small size and low power
TX Power: adjustable up to +14 dBm high efficiency PA, max PA boost up to 20dbm
Up to 15 km coverage at suburban and up to 5 km coverage at urban area

## Slide 40
LoRa_EVB
BootMode Button
User Button
Module Reset
LoRa Module UART Tx/Rx Select
Pin header
Arduino H/W
Compatible
Grove Sensor
Compatable
UART to USB Chip
Micro USB Socket
Arduino Reset
LoRa Module SWD
GND/SWCLK/SWDIO/VCC
UART PIN
Level Shift
XBEE compatible
SMA, U.FL Connector

## Slide 41
Module Hands-on
Baud Rate | 115,200bps
Data bit | 8bit
Stop bit | 1bit
Parity bit | None
Serial Terminal
Setup CP2102 USB Driver
Tools -> CP210x_Windows_Drivers.zip

## Slide 42
AT Commands
Procedure | Command to send | Parameter
Print AT Commands list | AT+MHELP | -
Set APPKEY (Only OTAA) | AT+LAK=… | 16 Bytes AppKey
Set NWSKEY (Only ABP) | AT+LNWSK=… | 32 Bytes NWSKEY
Set APPSKEY (Only ABP) | AT+LAPSK=… | 32 Bytes APPSKEY
Set APPEUI (Only OTAA) | AT+LAEUI=… | 8 Bytes AppEUI
Set DEVEUI (Only OTAA) | AT+LDEUI=… | 8 Bytes DevEUI
Set Confirmed Retrans Number | AT+LRCNT=5 | 1~8 Number
Set Unconfirmed Repit Number | AT+LUNREP=3 | 1~15 Number
Set Confirmed / Unconfirmed | AT+LCFM=1 | 0 = Unconfimred 1 = Confimred
Data uplink | AT+LSEND=1,1234 | Port number, Send data
Set Class | AT+LCLS=C | A = Class A B = Class B (Not Support) C = Class C
Set DataRate | AT+LDR=5 | 0~5 DataRate
Set ADR | AT+LADR=0 | 0 = ADR off 1 = ADR on
Join mode | AT+LJOIN=OTAA | OTAA = OTAA mode ABP = ABP mode
Module reset | AT+LRESET | -

## Slide 43
AT+MHELP

## Slide 44
LoRa Join procedure
Set the DevEui, AppEUI, and Appkey numbers on the board.
Check message
AT Commands | Comment
AT+LDEUI=000000000000000x | x : Kit Number
AT+LAEUI=0000000000000001 | APPEUI Fix
AT+LAK=0000000000000000000000000000000x | x : Kit Number
AT+LRESET | 

## Slide 45
LoRa_Data Send
Send Data
AT Commands | Comment
AT+LSEND=1,1234 | 

## Slide 46
LoRa_Data Send
Server Log

## Slide 47
LoRa_Data Receive
Server Log

## Slide 48
LoRa_Receive
Device Log
Message | Comment
at+recv=5,3,123456 | 5=Port Num 3=Data Length 123456=Data

## Slide 49: LoRa Application hand-on
Setup Development environment
Libraries
UnConfirmed Up Demo
Confirmed Up Hand-on
Downlink Demo

## Slide 50
Setup Development
environment

## Slide 51
Arduino Setup
Setup Arduino Sketch https://www.arduino.cc/download_handler.php
There is setup file in tools folder.

## Slide 52
Arduino USB Driver
USB Driver Setup
Tools -> USB_Driver -> CH341SER -> SETUP.EXE

## Slide 53
Arduino Libraries
Libraries folder copy.
Paste to my documents -> arduino -> libraries.

## Slide 54
Arduino Hello World
Open Firmware 1_Hello_World
Click icon to upload, Check upload complete message
Click the icon to open the serial monitor, Setting baudrate 115200
Check message output.

## Slide 55
H/W Setting
1. Move Jumper Cap to J6 UART_5V
2. Arduino Board and LoRa EVB Stacking
3. Remove 2 Jumper Caps from J5 Pinheader
4. Using the enclosed pinheader and wire Connect UART_RX <-> TX3 14 Connect UART_TX <-> RX3 15
5. Easy Shield Stacking
Connect
Jumper Cable
Move UART_5V

## Slide 56
H/W Setting
LoRa EVB + Arduino
Easy Shield

## Slide 57
Libraries

## Slide 58
Library
Function prototype | Comment | Example
int read( float& humidity, float& temperature); | Read humidity, temperature | dht11.read(humi, temp)
Function prototype | Comment | Example
int8_t after(unsigned long duration, void (*callback)(void)); | Run callback after duration. | send_t.after(10, send_timer_handler);
int8_t every(unsigned long period, void (*callback)(void)); | Always run callback periodically. | send_t.every(10, send_timer_handler);
void stop(int8_t id); | Stop timer | timeout_t.stop(timeout_timer_id);
void update(void); | Update timer | send_t.update();
DHT11 library
Timer-master library

## Slide 59
DHT11 Timer Library Test
Open DHT11_Timer_lib_test.ino. Complie and Upload

## Slide 60
LoRa Library
Function prototype | Comment | Example
void LoRaClass::init(Stream *LoRaSerial) | LoRa UART assign | LoRa.init(&Serial3);
int LoRaClass::available() | Check LoRa UART available | LoRa.available();
int LoRaClass::read() | Read LoRa UART | LoRa.read();
int LoRaClass::begin() | LoRa Reset & Check JOINED | LoRa.begin();
String LoRaClass::classType() | Get Class | LoRa.LoRaClass();
int LoRaClass::classType(int cls) | Set Class | LoRa.LoRaClass('C');
int LoRaClass::ADR(int adr) | Set ADR | LoRa.ADR(1);
String LoRaClass::DR() | Get DR | LoRa.DR();
int LoRaClass::DR(int dr) | Set DR | LoRa.DR(5);
String LoRaClass::devEUI() | Get DevEUI | LoRa.devEUI();
String LoRaClass::appEUI() | Get AppEUI | LoRa.appEUI();
int LoRaClass::retxConf(int count) | Set Confirmed ReTx | LoRa.retxConf(5);
int LoRaClass::Confirmed(int confirmed) | Set Confirmed | LoRa.Confirmed(1);
int LoRaClass::send(const char *data, uint16_t port) | LoRa Data | LoRa.send("1234", 5);

## Slide 61
Unconfirmed Up Demo

## Slide 62
Unconfirmed Uplink
Open _3_Unconfirmed_Uplink project. Complie and Upload
Unconfimred uplink temperature & humidity
Set Class C
ADR On
DataRate 5
Set Unconfimred
Repit count 3
Period 30 Sec

## Slide 63
Confirmed Up
Hands-on

## Slide 64
Confirmed Up
ACK Non-receipt
Count 10 over
Count under 10
ACK receipt
Enter Timout Handler
Increase Timeout CNT

## Slide 65
Downlink Demo

## Slide 66
Downlink
Open _5_Downlink project. Complie and Upload
Downlink Data 0x01

## Slide 67
Downlink

## Slide 68: Appendix
LoRa Gateway

## Slide 69
LoRa Gateway
RisingHF RHF0M301
http://www.risinghf.com/product/risinghf-iot-dicovery/?lang=en

## Slide 70: Q&A 감사합니다